## Slide 1: CURRENT CONTROLLED PWM INVERTERS
References
Modern power Electronics and AC Drives by B K Bose
Modern power Electronics Evolution, Technology and Application
By B K Bose

## Slide 2
Problems associated with voltage controlled inverters
PWM output voltage waveform causes current ripple. This increases motor losses.
Extra current rating is required for devices.
A small unbalance in motor phase voltage leads to relatively large unbalance in motor current.
This causes extra heating and torque ripple in motor output.
Such constraints lead to high degree of precision for a fairly smooth sinusoidal waveform generation.

## Slide 3
In drive systems, flux and developed torque depends on current and hence current control is important.
Objectives of Current Control Scheme:
Minimization of motor losses so that conventional motors can be used without derating.
Minimization of peak device current.
Simplification of control scheme to reduce cost.
These objectives can be met with independent current
control on each inverter output phase

## Slide 4
Reference sine wave at the desired output frequency and proportional to desired current amplitude is generated.
Actual motor current is compared with these reference waveforms.
If TA+ is on and the motor current is positive and more than the reference,
TA+ is turned off and TA- is turned on.
But the positive load current flows through DA- and lower source.
Current magnitude decreases.
When load current becomes lower than reference value, TA+ is turned on and current magnitude increases.

## Slide 5
ia ref
ia

## Slide 6
problem associated with this scheme is the maximum operating frequency of the inverter.
Inverter losses are proportional to frequency and must be limited.
This can be achieved by introducing a small amount of hysteresis into the comparator.

## Slide 7: Hysteresis Band Current Controlled PWM
Hysteresis band PWM is a current feedback control method of PWM.
actual current track the command current within a hysteresis band.
The control circuit generates the sine reference current wave of desired magnitude and frequency.
It is compared with actual phase current wave.

## Slide 8
io
i0*
During positive half cycle of load current, TA+ conducts and i0 rises. When the current exceeds a prescribed hysteresis band then TA+ is turned Off and lower switch is turned ON.
As the current crosses the lower band limit, the upper switch TA+ is turned on again.
But DA- conducts. i0 decreases
The output voltage changes from -0.5 Vd to +0.5 Vd and the load current starts to rise.
Vo
Vd/2
TA+
DA-
TA-
DA+
TA-
DA+

## Slide 9
When Vn < Vp, V0 = +Vsat
When Vn > Vp, V0 = - Vsat
Vp
Vn
V0

## Slide 10
When TA+ is on, current rises
When DA- is on, TA+ is off

## Slide 11
Switching period of TA+ is
Switching frequency
For a fixed tolerance band of current ΔI, switching frequency fs depends on back emf Ec

## Slide 12
When Ec = 0, fs is maximum
Switching frequency
When Ec varies sinusoidally, Ec = m sinωt

## Slide 13
For a fixed tolerance band ΔI, switching frequency fs varies with time around an average value at a frequency twice as that of the back emf Ec
ΔI is selected such that fs remains in the permitted value of the device.

## Slide 14
Factors that influence switching frequency:
Induced counter emf of the load
Dc bus voltage
Current ripple.
Effect of DC voltage limit:
There must be sufficient input dc source potential to force line currents in the desired direction.
For low values of load back emf, magnitude of input dc source potential is not critical.
For high motor speed (large value of back emf EC) the inverter must be capable to command the desired current.