## Slide 1: Line Frequency Controlled Rectifiers
Controlled dc output voltage
varies from +ve maximum to –ve maximum.
Controllable devices like thyristors, IGBT BJT are used.
Commutation of the devices depends on the ac side line frequency.
Hence the name line frequency rectifiers.

## Slide 2
Dc side current is always +ve
Dc side voltage is +ve or -ve.
+ve voltage and +ve current at dc side indicates rectification mode. Power flows from ac side to dc side.
operating points lie in the first quadrant of Vd-Id plane.
Vd Average voltage at DC side
Id Average current at DC side
-ve voltage and +ve current at dc side indicates inversion mode. Power flow is from dc side to ac side.
operating points lie in the fourth quadrant of Vd-Id plane.

## Slide 3: Single phase half wave controlledrectifier
R load
0 → α
T1 is off.
i =0.
At ωt = α , T1 is triggered on
α → π
T1 is on.
vd = vs i =vd/R = vs/R =
is = i
At ωt = π, i = 0
π →2π
T1 is off.
i = 0. vd = 0. is = 0 vT1 = vs
T1
is

## Slide 4: R-L load
0 → α
Switching device is off.
i = 0 Vd = 0
VL = 0 , VR = 0
VT = vs
α → θ2
Thyristor is on.
Vd = = vs =
i =
vR (t) = Ri(t)
vL (t)= vs- vR (t)
At ωt= θ1
di/dt = 0, vL = 0,
vR = vs
Area A1 = Area A2
Energy stored in the inductor during α to θ1 is sent back to ac source during θ1 to θ2

## Slide 5: R-L load with a freewheeling diode
id
↓

## Slide 6
L-E load
0 → θ
T is reverse biased.
i = 0
VL = 0
Vd = Ed
VT = vs - Ed
At α Thyristor is forward biased and triggered.
α →β
Thyristor is conducting.
Vd = vs
VL =L di/dt = vs - Ed
VT = 0
θ → α
T is forward biased and off.
i = 0
Vd = Ed
VL =0
VT = vs - Ed

## Slide 7
At β, i = 0, T becomes off.
β → 2π
Thyristor is off
i = 0
VL = 0
Vd = Ed
VT = vs - Ed

## Slide 8
R-E load
θ → α
Thyristor is forward biased and in the off state.
id = 0
vd = Ed
vR =0
vT = vs - Ed
α →∏- θ
Thyristor is forward biased and in the on state.
Vd = vs
vR =Ri = vs - Ed
i = (vs - Ed )/R
VT = 0
0 → θ
Thyristor is reverse biased.
id = 0
vd = Ed
vR = 0
vT = vs - Ed

## Slide 9
At ∏- θ,
id = 0
Thyristor becomes off
∏- θ → 2∏
vd = Ed
vR =0
vT = vs - Ed

## Slide 10: Single phase Fully Controlled bridge rectifier
R Load

## Slide 11
R – L Load
Discontinuous load current mode
α → θ1
T1 and T2 conduct
θ1 → π+α
is = id = 0 , vd = 0
T1 T2 T3 and T4 remain in the off state
vd = vs
id =
is = id
vT1 =0, vT2 =0
vT3 =
At ωt=θ1 , id =0
iT1 = iT2 =0
Both T1 and T2 go to the off state

## Slide 12
π+α → π+θ1
vd = = -vs
id =
is = - id
vT1 = vs= vT2
At ωt = π +θ1 , id =0
iT3 = iT4 =0
Both T3 and T4 go to the off state
π+θ1 → 2π+α
T1 T2 T3 and T4 remain in the off state
is = id = 0 , vd = 0,
T3 and T4 conduct

## Slide 13
R – L Load, Continuous Current Mode
For ωt < α, T3 & T4 were conducting
T1 and T2 are turned on
T3 and T4 are line commutated
α →∏ + α
T1 and T2 conduct. T3 and T4 are in the off state
Vd = Vs =
id =
is = id
VT3 = - vs = VT4
At ωt = α, id = I1 (≠0)

## Slide 14
At ∏ + α, T3 and T4 are turned on
T1 and T2 are line commutated
∏ + α → 2∏ + α
T3 and T4 conduct.
Vd = - Vs
        is = -id
VT1 = vs = VT2

## Slide 15
R – L Load, constant load current Id
α →∏ + α
T1 and T2 conduct,
T3 and T4 are line commutated
Vd = Vs
is = Id
VT3 = - vs = VT4
∏ + α →2∏ + α
T3 and T4 conduct,
T1 and T2 are line commutated
Vd =- Vs
is = -Id
VT1 = vs = VT2

## Slide 17: Performance parameters
DC Side
Average load voltage
VdRMS
Average Power through the converter =
P=Vdavg Id = 0.9VsIdcosα
Ripple frequency = twice the line frequency
Voltage Ripple Factor Kv =

## Slide 19
RMS value of is1 Is1 =
RMS value of nth harmonic isn Isn =
n = 3, 5, 7,……
RMS value of total source current is
Is = Id

## Slide 20
Harmonic spectrum

## Slide 21
Total harmonic distortion THD =
%
Displacement factor
DF = cos(-α) = cos α
Ac side Power factor =

## Slide 22
Power at the source side
Total apparent Power S = VsIs
Active Power P
Fundamental frequency current results in fundamental reactive volt amperes
            Q1 = Vs Is1sinφ1 = Vs Is1sinα
Fundamental frequency apparent power
S1= Vs Is1

## Slide 23
Vdavgα/ Vdavg0

## Slide 24: Effect of source inductance
The current commutation takes a finite time called µ or commutation interval
constant load current Id
0 → α
T3 and T4 are on
T1 and T2 are off
vd = -vs
id = Id
is =- Id
VT3 = 0 = VT4
VT1 = vs = VT2
At α , T1 and T2 are turned on

## Slide 25
α → α + μ
iT3 and iT4 decrease from Id → 0
iT1 and iT2 rise from 0 → Id
T1 , T2, T3, T4 are on
Vd = 0, id = Id
is varies from –Id to → Id.
vLs = vs
At (α + μ), iT3 = 0 = iT4 T3 and T4 are turned off naturally

## Slide 26
α + μ → ∏ + α
T1 and T2 are on
T3 and T4 are off
vd = vs
id = Id
is = Id
VT1 = 0 = VT2
VT3 =- vs = VT4
At ∏ + α , T3 and T4 are turned on

## Slide 27
∏ + α → ∏+ α + μ
iT1, iT2 decreases from Id → 0
iT3, iT4 rises from 0 → Id
T1 , T2, T3, T4 conduct
Vd = 0, id = Id
is varies from +Id to → - Id.
vLs = vs
At (∏ +α + μ), iT1 = 0 = iT2 T1 and T2 are turned off

## Slide 28
∏ +α + μ → 2∏ + α
T3 and T4 are on
T1 and T2 are off
vd = - vs
id = Id
is =- Id
VT1 = vs = VT2
VT3 = 0 = VT4
vLs = 0

## Slide 29
During the commutation period µ, T1, T2, T3 and T4 are on

## Slide 30
Average o/p voltage =

## Slide 31: Practical thyristor converters
Shape of the load current depends on
load parameters and firing angle.
When T1 and T2 are conducting,
Discontinuous Load Current Mode
id(ωt) =
K =
id(ωt) =
Z=.
𝛟=tan-1
At ωt = α, id(ωt) = 0

## Slide 32
id(ωt) =

## Slide 33
Average value of Vd is approximately
Idmin is the minimum value of id that
occurs at ωt=α
Instantaneous value of load voltage
In steady state, id(0) = id(T)
In terms of average values,
Vdavg = rdId + Ed
By controlling α, Id and hence power delivered to the load can be controlled.
Continuous current mode

## Slide 34: …

## Slide 35
Inverter mode of RectifierBridge

## Slide 36: Inverter mode of operation
Average value of Vd is negative for
Power flows from dc load to ac source side
Pdc =Vdavg Idavg is negative
Pac =Vs Is1 cosФ1 is negative as
The voltage source on dc side can be
battery / photovoltaic source /
wind-electric generating system

## Slide 38
Assuming constant Id, and as drop across Ld is zero
Ed = Vd =
The extinction angle γ of thyristor is =
Extinction time interval should be greater than thyristor turn off time tq