## Slide 1: Linear power converters
Advantages
Simplicity in Design
No electrical noise in the output
Fast dynamic response time
Low cost
Disadvantages
Both input and output are of the same range.
only one output
Low efficiency

## Slide 2: RESONANT CONVERTERS

## Slide 3: High Frequency Switch mode PWM Converters
Advantages
Higher efficiency
Devices operate at the maximum efficient points like cut off and saturation points
Multi-output is possible
Size and cost are much lower especially at high power levels.

## Slide 4
Limitations
Greater circuit complexity compared to linear converters
  Controllable switches (operated in a switch mode) are required
  to turn on and turn off the entire load current during each switching.
occurrence of large di/dt and dv/dt during switching.
Hence high electromagnetic interferences.
High stress levels on devices that
increases linearly with the switching frequency of the PWM.
Higher switching losses at high frequencies.

## Slide 5: Dissipative snubbers circuits:
The switch stresses can be reduced by connecting simple dissipative circuits in series and parallel with the switches in the switch-mode converters.
These snubbers shift the switching power loss from the switch to the snubber circuit and therefore do not provide a reduction in the overall switching power loss.
Switching loci with snubbers Dissipative snubbers circuits

## Slide 6
To minimize these problems, switches are made to change the states of turn on to turn off or vice versa when the voltage across it or current through it is zero at the switching instant.
These topologies require some form of LC resonance and hence, they are classified as resonant converters.
The switch voltage and current are shaped so as to get zero voltage and/or zero current during switching and they are known as soft switching converters.

## Slide 7
Advantages of soft switching resonant converters
Reduced power loss at high switching frequency
Less size and hence high power density
High efficiency
Less stress on the devices

## Slide 8
Classification of Resonant converters
Resonant converters
  Load-resonant converters
  Resonant-switch converters
  Resonant-dc-link converters
  High-frequency-link integral-half-cycle converters
  Voltage-source series-resonant converters
Series Loaded Resonant converters
Parallel Loaded Resonant converters
Hybrid converters
Current-source parallel-resonant converters
Class E and subclass E resonant converters
ZCS converters
ZVS converters
ZVS-CV converters
Resonant-switch dc—dc converters

## Slide 9: Resonant switch converters
Additional circuit elements are added to get zero voltage/zero current switching and are called resonant switch converters.
zero current switching (ZCS) topology
zero voltage switching (ZVS) topology
zero voltage switching, clamped voltage (ZVS--CV) topology

## Slide 10
LC resonance is utilized to shape the switch voltage and current to provide zero-voltage and/or zero-current switching.
During one switching period, there are resonant as well as non-resonant operating intervals. Therefore, these converters are also known as quasi-resonant converters.

## Slide 11: zero current switching (ZCS) Converters
The switch turn on and turn off occurs at zero current.
Lr and Cr are the are the resonant elements used to get zero current turn on and turn off conditions.

## Slide 12
Initial Conditions
Let the switch is in the off state.
Diode is in the on state.
Vc = Vd, iT = 0
At t = t0 switch is turned on
Due to the presence of inductance, turn on occurs at zero current.
Lr and Cr are shorted through the switch
Voi = Vd - Vc
= 0
Diode continues to conduct.
VLr = Vc = Vd

## Slide 13
t0 → t1
vLr = Vd
iT rises linearly.
iT is less than iLf.
iD =
D continues to conduct until iT is equal to iLf.= I0
Vc =
At t = t1,
iT is equal to iLf
D stops conducting.
Lr and Cr form a parallel resonant circuit.

## Slide 14
t1 → t1’
Cr discharges from Vd to zero through switch and Lr
iT =
At t1’ iT and ic are at their peak values.
Vc reaches zero
t1’
t1’

## Slide 15
t1’ → t1’’
ic decreases sinusoidaly to zero
At t1’’
Vc reaches - Vd
ic = 0
iT = I0
t1’
t1’
t1’ ’
t1’ ’

## Slide 16
Capacitor discharges sinusoidaly
in the negative direction.
iT =
iT reduces to zero sinusoidaly.
Switch is turned
off naturally
turn off occurs at zero current.
t1’
t1’ ’
t1’ ’
t2

## Slide 17
t2 → t3
Capacitor discharges through the load circuit
ic =
Vc rises linearly to Vd
At t = t3
Vc = Vd
Vdiode= 0
Diode conducts
Off period of the converter begins
t1’ ’
t1’ ’
t2

## Slide 18
t3 → t4
Switch is off.
Load current freewheels through
diode
Vc = Vd
iT = 0
At t4 gate pulse is given to switch
to begin next cycle

## Slide 19: zero voltage switching (ZVS) Converters
The switch turn on and turn off occurs at zero voltage.

## Slide 20
Initial condition
the switch is in the on state. D is off
Vc =
iL =
V0i =
At t = t0 switch is
turned off
Due to the presence of
capacitance,
turn off occurs at zero voltage.
t0 → t1
iL which is constant load current flows through the capacitor
Vc rises linearly from zero to Vd
At t = t1, Vc = Vd
V0i =
D starts conducting
t1
t1

## Slide 21
t1 → t1’
Switch is off and D is on.
Cr & Lr resonates
C gets charged to a potential greater than Vd due to negative voltage across Lr
Vc > Vd
At t1’
t1’ → t1’’
Capacitor discharges through dc source, D and Lr
iL reverses sinusoidaly due to Lr – Cr resonance.
iD =
iL = - I0 At t2 Vc = 0
VDr = 0
t1
iL is zero
Vc is maximum =
Vd + VLr
-
At t1’’ Vc = Vd

## Slide 22
Dr starts conducting.
Vc continues to be at zero
t2 → t2’
D & Dr conduct.
Vcr = 0
iL rises linearly to zero through Dr.
At t2’ , iL = iDr = 0,
Gating signals are applied to the switch during this interval
Vcr continuous to be at zero potential and the turn on occurs at zero voltage.
Peak voltage across the switch is 2Vd
VLr = Vd
VLr = Vd
Switch is reverse biased while Dr is conducting
Dr becomes off and switch goes to the on state

## Slide 23
Switch becomes on at
t2’ when iL = iDr = 0 and
Dr is off.
Vc remain at zero.
Turn on occurs at zero voltage condition
t2’ → t3
iD = zero, D becomes off
VLr = Vd
iL rises linearly to I0
D is still conducting.

## Slide 24
t3 → t4
iL = IT = I0
Vc = 0
V0 = Vd
At t4 switch is turned off again at zero voltage

## Slide 25: Zero voltage switching clamped voltage (ZVS-CV) Topology
Switches turn on and turn off at zero voltage.
Peak voltage across the switch is clamped to the input dc voltage
Cf is considered as very large and hence load is replaced by the voltage source V0

## Slide 26
Initial condition
T+ is on. T- is off.
VL = (constant)
iL rises linearly
= VC+ voltage across C+ is zero
VC- =
VT+ = 0
At t = t0, T+ is turned off at zero voltage due to VC+
iL
voi

## Slide 27
t0 → t0’
C+ = C- = ½ C are selected as of small values. The resonant frequency f0 = 1/(2π) is very large compared to switching frequency.
Lf/C is very large and variation in IL is very small.
iL = I0 = iC+ + iC-
T+ , T-, D+ and D- are in the off state
C- has an initial voltage of Vd
equivalent circuit
Thevenin equivalent circuit
C = C+ + C-

## Slide 28
VC+ changes linearly from 0 to Vd
VC- = Voi = decreases linearly from Vd to zero
C+ = C-
iL
voi

## Slide 29
At t = t0’,
D- starts conducting
iL decreases linearly to zero at t0’’
T- is gated while D- is conducting.
T- starts conducting when D- becomes off due to zero iL at t0’’
t0’’ → t1
iL flows through T-
vL = - v0
vc- = 0 = voi = vD-
vL = - v0
iL
voi
Maximum voltage that comes across T+ is Vd
At t1 T- is turned off.

## Slide 30
t1 → t1’
T+ and T- are off.
Negative iL flows through C-
C+ discharges from Vd to 0
C- gets charged from 0 to Vd.
t1’ → t2
When VC+ is zero, D+ conducts negative iL.
VL =
VC- = Voi = Vd
T+ is gated while D+ is conducting.
T+ starts conducting when D+ becomes off when iL is reduced to zero at t2
iL
voi

## Slide 31
t2 → t3
T+ becomes on at
zero voltage condition.
VL =
iL rises positively through T+ and load.
iL
voi

## Slide 32: LOAD-RESONANT CONVERTERS
Consist of an LC resonant tank circuit
A series LC or a parallel LC circuit can be used to produce oscillating voltage and current.
Converter switches can switched at zero voltage and/or zero current.
These converters can be sub-classified as :
A. Voltage-source series-resonant converters
(a) Series-loaded resonant (SLR) converters
(b) Parallel-loaded resonant (PLR) converters
(c) Hybrid-resonant converters
B. Current-source parallel-resonant converters
C. Class E and subclass E resonant converters

## Slide 33: SERIES-LOADED RESONANT (SLR) dc-dc CONVERTERS
The series-resonant tank is formed by Lr and Cr
Current through the resonant tank circuit is full-wave rectified at the output
feeds the output stage
Output load appears in series with the resonant tank
Output voltage can be assumed to be a dc voltage without any ripple because of large Filter capacitor Cf
Half-Bridge SLR converter

## Slide 34
The output voltage Vo is reflected across the rectifier input as VB’B
VB’B = Vo if iL is positive
= - Vo if iL is negative
Resistive power loss in the resonant circuit is assumed to be negligible

## Slide 35
For iL > 0
If T+ conducts
If D- conducts
When iL is positive, it flows through T+ or through the diode D-

## Slide 36
For iL < 0
If T- conducts
If D+ conducts
When iL is negative, it flows through T- or through the diode D+

## Slide 37
The average output voltage V0 cannot exceed Vd/2

## Slide 38
The switching frequency (fs) with which the circuit waveforms repeat, can be controlled to be less than or greater than the resonance frequency (fo)
The ratio (fs/foor /) determines the nature of iL
(continuous or discontinuous).
Modes of operation
  (1) Discontinuous-Conduction Mode with
  (2) Continuous-Conduction Mode with
  (3) Continuous-Conduction Mode with

## Slide 39
Discontinuous-Conduction Mode with
Ts/2 > T0
Initial conditions
Vc = - 2v0
iL = 0
At ω0t0, T+ is turned on.
ω0t0 → ω0t1
iL rises from zero and
vc builds up from -2V0.
At ω0t0, VL =

## Slide 40
At ω0t1 iL becomes zero and T+ becomes off
VL (ω0t1) =
Vc (ω0t1) =

## Slide 41
iL reverses and flows through D+
VL (ω0t1) =
At ω0t2, iL becomes zero
and D+ becomes off.
VL (ω0t2) =
Vc (ω0t2) =

## Slide 42
ω0t2 → ω0t3
All devices are off.
iL = 0
Vc = 2V0

## Slide 43
At Ts/2 = ω0t3,
T- is turned on.
iL is negative.
At (ω0t3 + π) iL becomes
zero and T- becomes off
iL reverses in the positive
direction through D-

## Slide 44: (1) Discontinuous-Conduction Mode with

## Slide 45: (2) Continuous-Conduction Mode with

## Slide 46: (3) Continuous-Conduction Mode with

## Slide 47
Steady-state characteristics of an SLR
Control of SLR dc—dc converter

## Slide 48: PARALLEL-LOADED RESONANT (PLR) dc-dc CONVERTERS
The series-resonant tank is formed by Lr and Cr
Output load appears in parallel with the resonant tank
Half-Bridge PLR converter

## Slide 49
The voltage across the resonant-tank capacitor Cr is rectified, filtered, and then supplied to the load
Current through the output filter inductor is assumed to be a ripple-free dc current Io during a switching frequency time period (at high switching frequency and a sufficiently large value of the filter inductor)
The voltage across the resonant tank depends on the devices conducting as follows:
T+ or D+ conducting: VAB = +1/2 VD
T- or D- conducting: VAB = -1/2 VD
Equivalent circuit

## Slide 50: MODES OF OPERATION (1) Discontinuous-Conduction Mode

## Slide 51: (2) Continuous-Conduction Mode with

## Slide 52: (3) Continuous-Conduction Mode with

## Slide 53: (c) Hybrid RESONANT dc-dc CONVERTERS
This topology consists of a series-resonant circuit
load connected in parallel with only part of the capacitance, for example, one-third of the capacitance, and the other two-thirds of the capacitance appears in series.
Have the advantageous of both the SLR and the PI-R converters
  SLR convener offers an inherent current limiting under short circuit conditions
  PLR converter acts as a voltage source and thus regulating its voltage at no load with a high-Q resonant tank is not a problem.

## Slide 54: 1(B) CURRENT-SOURCE PARALLEL-RESONANT DC-AC INVERTERS FOR INDUCTION HEATING
a square-wave current source is applied to a parallel-resonant load
The induction coil and the load (RL combination) are modelled by means of a parallel combination of equivalent Rload and Lr, rather than a series RL.
The capacitor Cr is added to resonate with Lr in parallel.
It is assumed that the harmonic impedance of the parallel-resonant load at the harmonic frequencies of the input current source is negligibly small, thus resulting in an essentially sinusoidal voltage vo.
circuit phasor diagram

## Slide 55: Current-source parallel-resonant inverter for induction heating:
A small inductance Lc ( in series with resonant load) is used to avoid a large di/dt (during current commutation) through the inverter Thyristors
The inverter output current io therefore deviates from its idealized square-wave shape and becomes trapezoidal
Power output of this inverter is controlled by controlling its switching frequency or DC current Id
After the thyristor stops conducting, a reverse voltage appears across it for a time interval equal to γ/ωs and thyristor has to block a forward-polarity voltage.
Therefore, γ/ωs should be sufficiently than the turn-off time tq of the
thyristor
(a) circuit (b) waveforms

## Slide 56: 1(C) CLASS E CONVERTERS
Load is supplied through the sharply tuned series-resonant circuit
which results in a sinusoidal output current.
The input to the converter is fed through a sufficiently large inductor
Therefore, in steady state, the input to the converter is a dc current source Id (where the current magnitude depends on the power output)
Advantages
  Elimination of switching losses
  Reduction in EMI
  Produces a sinusoidal output current with a single-switch
Disadvantages:
  high peak voltage and current associated with the switch
  Large voltages and currents through the resonant LC elements
It is possible to obtain a dc—dc voltage conversion by rectifying the output current.
  Used for high-frequency electronic lamp ballasts.
Since the output load may vary over a large range, an impedance matching network is required between the output of the class E converter and the output rectification stage to ensure a lossless switching operation of the class E converter

## Slide 57
When the switch is on: Id + io flows through the switch
When the switch is turned off:
Because of the capacitor Cl , the voltage across the switch builds up slowly, thus allowing a zero-voltage turn-off of the switch.
Voltage across capacitor Cl builds up, reaches its peak, and eventually comes back to zero, at which instant the switch is turned back on.
A class E converter operates at a switching fs, which is slightly higher than the resonant frequency fo
During the interval when the switch is off, the input supplies to the circuit since VT is positive
The average value of VT equals Vd.
If io is assumed to be purely sinusoidal,
the average voltage across the load
resistance R is zero.
The average voltage across Lr is also zero in steady state.
Therefore, Cr blocks the dc voltage Vd in addition to providing a resonant circuit.

## Slide 58: Class E converter: Modes
Optimum mode
Switch voltage returns to zero with a zero slope (iC1 = 0)
Load resistance R be equal to an optimum value Ropt.
No need for a diode in antiparallel with the switch.
The switch duty ratio D = 0.5 results in a maximum power capability (maximum switch utilization ratio)
Non-Optimum mode
Switch voltage reaches zero with a negative slope
dVT/dt < 0 and iC1=Cl (dVr/dt) < 0
R < Ropt
A diode is connected in antiparallel with the to allow this current to flow while keeping the switch voltage at zero (at one diode drop).
Switch is turned on as soon as the diode starts to conduct.

## Slide 59: Class E converter: Optimum mode

## Slide 60: Class E converter: Non-optimum mode

## Slide 61: Advantages of resonant converters:
Solution to the problem faced in hard-switched (PWM-type) converters, as they allow zero-current or zero-voltage switching.
Circuit operation is possible at higher frequency, reducing the size of reactive components.
Owing to smooth waveforms of voltage and current, noise and interference effects are reduced.
Stresses on the switching devices also reduce because of zero-voltage/zero-current switching.
HF transformer non-idealities can be incorporated as a part of circuit itself.
Operation even under output short-circuit condition is possible.