## Slide 1
The inverters are generally classified into
Voltage Source Inverter (VSI) which produces a defined voltage waveform for the load.
Current Source Inverter (CSI) which outputs a defined current waveform for the load .

## Slide 2: CURRENT SOURCE INVERTERS (CSI)
Current Source (Front end of the CSI)
consists of
a controlled rectifier bridge or a dc chopper.
A filter is connected to obtain ripple free output current.
Inverter
converts direct current at the input to an alternating current at the output.
Frequency and magnitude of the output are controlled by the control circuitry of the inverter.
output load has a defined current waveform
Power transfer takes place between an adjustable direct current source and an ac load

## Slide 3
CSI from ac source

## Slide 4
CSI from dc source

## Slide 5
Two types of CSI are commonly used in the MV drive:
1. load-commutated inverter (LCI).
2. PWM inverters
LCI employs thyristors whose commutation is achieved by additional commutating circuits.
suitable for very large synchronous motor drives with a power rating up to 100 MW.
The PWM inverter uses switching devices with self-extinguishable capability.

## Slide 6
Load Commutated Inverter (LCI)
Single Phase CSI with Ideal Switches
Load current has definite shape
Load voltage waveform depends on the nature of load

## Slide 7
Three Phase CSI with Ideal Switches

## Slide 8: Single Phase Capacitor Commutated CSI
    Capacitor is used to commutate the devices.
    For t < 0, S3 & S4 were conducting.
    io was negative
    vc = -v1
    At t = 0, S1 & S2 are turned on

## Slide 9
0 < t < T/2
S1 & S2 are on
Vc increases from -v1 to +v1.
vo = vc
io = vc/R, iac = Idc
vin = vc
ic = iac - io = Idc - io
iS1 = Idc = iS2
vS1 = 0
At t =T/2, S3 & S4 are turned on.
S1 & S2 are turned off due to vc.

## Slide 10
T/2 < t < T
S3 & S4 are on
Vc changes from +v1 to -v1
.
io = vc/R, iac = -Idc
vo = vc vin = - vc
vS1 = vc
ic = iac - io = -Idc – io
iS3 = Idc = iS4

## Slide 11
iac has definite shape and resolved into its Fourier Components.
Fundamental component of iac is at the frequency of 1/T
Period T is determined by the gating circuit.
Higher order harmonics are bypassed through the capacitance.
Load current and voltage waveforms depends on the relative values of Rand C

## Slide 12: Time Domain Analysis
0 < t < T/2
At t = T/2, i0(t) = +I1

## Slide 13
tc is the turn off time provided by the circuit for a device.
Vc at t = tc is 0
i0(t)R at t = tc is 0

## Slide 14: Square wave mode
At low values of inverter frequency, I1 =
Idc and load current approximates square wave.
To get square wave, T must be > 10 RC
Also,
If tq is the turn off time of the devices used, then, tc should be greater than tq.
minimum value of tc should be tq.
minimum value of 0.69RC should be tq.
Minimum value of C must be tq / 0.69R
C is selected as
R is the available load resistance
C = tq / 0.69R

## Slide 15
To get square wave, T must be > 10 RC
To get square wave load current,
For a given load R and device turn off time tq,
C is selected as C = tq / 0.69R and
maximum frequency of operation is limited to 0.069/tq

## Slide 16: Sine wave mode of output current
For higher range of frequency, capacitance offers low impedance for harmonics and load current approximates sine wave.
Third harmonic is the most dominant harmonic.
C is selected such that its impedance for third harmonics XC3 is less than 50% of R at minimum value of the range of frequency.
All higher harmonics will be bypassed from load resistance to capacitance.

## Slide 17
Maximum frequency of operation is limited such that
turn off time tc provided by the circuit
is greater than device turn off time tq

## Slide 18: Single Phase Load Commutated CSI with Purely inductive Load

## Slide 19
At low frequency of inverter operation, Output Current waveform approximates Square waveform. This low frequency range is called No overlap region.
At higher frequency of inverter operation, Output Current waveform approximates Sine waveform. This frequency range is called Fully overlap region
Frequency range greater than no overlap region and lesser than fully overlap region is called Partial overlap region of frequency

## Slide 20
CSI in No-Overlap frequency range
One cycle of load current
is divided into 6 modes.
Prior to mode 1,
S1 and S2 were conducting
Load current path was
S1, D1, load, D2 and S2.
For t ≤ 0 ,
i0(0) = Idc, Vc(0) = -Vco
ic(0) = 0

## Slide 21
Mode -1
S3 and S4 are turned on.
S1 and S2 are turned off
due to –VCO .
Load current remains at Idc
Current path is
Current source, S3 , C, D1,
load, D2, C, S4.
VC varies linearly due to constant current Idc

## Slide 23
Mode -2
When Vc = 0, D3 and D4 become on.
L & C are shorted through D1, D2, D3 and D4 .
Current enters to L, C parallel circuit
through S3 and leaves through S4
By KCL,
2ic
V0 = -Vc

## Slide 24
Mode 2 ends when ic = 0
i0 = - Idc
Duration for Mode -2
t2 = π/2ω0
Current Commutation Interval
tc = t1 + t2
As ic = idiode= 0, D1 and D2 become off.

## Slide 25
Mode -3
Current path is
Source, S3,D3, load, D4,
and S4
ic = 0
i0 = -Idc
This mode continues till
S1 and S2 are turned on at T/2.
t3 = T/2 - (t1+t2)
= T/2 - (1+π/2)/ω0

## Slide 26: Transition Diagram of 1Ф CSI in No-Overlap Region of Frequency
For No-Overlap range of Frequency, sequence of operating modes is 1,2,3,4,5,6
Commutation interval
tc =
Duration of mode3
t3 =

## Slide 27
When inverter frequency is increased, T is decreased and t3 is also decreased.
At the limiting value of no overlap range of frequency, t3 becomes zero.
TNL is the minimum period for no overlap condition.
Maximum frequency limit for no overlap condition.

## Slide 28: PARTIAL OVERLAP FREQUENCY RANGE
Inverter Frequency is greater than fNL
Modes 3 and 6 are absent.
For t < 0, the inverter
was in mode 5.
S1,S2,D1,D2,D3,D4 were
Conducting.
Load current was oscillatory.
ic and vc were –ve, i0 is +ve

## Slide 29
At t = 0, S3,S4 are turned on.
S1,S2 are turned off.
This results in mode 2 operation.
ic becomes +ve and rises in the
+ve direction.
i0 which is +ve rises to a
constant value Idc
Vc rises with a +ve slope.
Drop across the load becomes
zero due to constant current of Idc .
D3, D4 are turned off.

## Slide 30
This results in mode1 operation.
Current path: source, S3, C, D1, load, D2, C ,S4
Mode1 ends when vc = 0
D3, and D4 are brought
into conduction resulting
mode 2 condition.
Vc rises in the +ve direction
i0 reverses to a value
less than Idc

## Slide 31
In partial overlap condition, Sequence of modes in one cycle is 2,1,2,5,4,5
Maximum frequency limit for partial overlap condition is

## Slide 32: FULLY OVERLAP CONDITION
If the inverter frequency is further increased, all the diodes conduct continuously resulting in sine wave load current.
In fully overlap condition, Sequence of modes in one cycle is 2,5

## Slide 33: PWM IN THREE PHASE CURRENT SOURCE INVERTER
The inverter produces a defined PWM output current iw.
DC side of the inverter is an ideal dc current source Id.

## Slide 34
The CSI requires a three-phase capacitor Cf at its output for the commutation of the switching devices.
The capacitor provides a current path
for the energy trapped in the load
inductance which would otherwise
cause high-voltage spike leading to
the damage of the switching devices.
The capacitor also acts as a harmonic
filter, improving the load current and
voltage waveforms.
The capacitor value can be reduced with the increase of the switching frequency.

## Slide 35
The dc current source Id can be realized by a voltage source rectifier with a dc current feedback control.
To make the dc current Id smooth and continuous, a dc choke Ld is used.
The magnitude of Id is kept at a value set by its reference Id* by the feedback control scheme.

## Slide 36
Switching pattern for the CSI should satisfy the following conditions.
1. Id should be continuous
two devices one from top group and
one from bottom group should conduct at a time.
  If only one device conducts, then there is no
  path for continuous current and high
  voltage will be induced by the dc choke.
  This causes damage to the switches.
  2. inverter current iw should be defined
If S1, S2 and S3 are conducting at a time,
the currents in S1 and S3, equal to the
PWM currents in the inverter phases A and B which is load-dependent.
sum of the two currents is equal to Id.
  If more than two devices conduct at a time,
  then load phase currents are not defined by
  switching pattern.

## Slide 37: SPACE VECTOR MODULATION
Only two switches, one from upper group and one from lower group, in the inverter conduct at a time.

## Slide 38
Three Zero states
1,4 3,6 5,2
DC side current is bye passed.
iwA = 0, iwB = 0, iwC = 0
Bypass operation.
Type of state | Switching state | On-state switch | Inverter PWM current |  |  | Space vector
 |  |  | iwA | iwB | iwC | 
Zero States | 1,4 | S1,S4 | 0 | 0 | 0 | 
 | 3,6 | S3,S6 | 0 | 0 | 0 | 
 | 5,2 | S5,S2 | 0 | 0 | 0 | 

## Slide 39
Six Active states
Type of state | Switching state | On-state switch | Inverter PWM current |  |  | Space vector
 |  |  | iwA | iwB | iwC | 
Zero States | 1,4 | S1,S4 | 0 | 0 | 0 | 
 | 3,6 | S3,S6 | 0 | 0 | 0 | 
 | 5,2 | S5,S2 | 0 | 0 | 0 | 
AA | 6,1 | S6,S1 | Id | -Id | 0 | 
Active
states
Load is 3 phase balanced
Three phase currents can be transformed into two phase currents in the α-β plane.
Current space vector can be expressed in terms of two phase currents as
Substituting for Iα and Iβ
For switching state [6 1], S1 and S6 are on

## Slide 40
Six Active states
Active States | 2,3 | S2,S3 | 0 | Id | -Id | 
Type of state | Switching state | On-state switch | Inverter PWM current |  |  | Space vector
 |  |  | iwA | iwB | iwC | 
Zero States | 1,4 | S1,S4 | 0 | 0 | 0 | 
 | 3,6 | S3,S6 | 0 | 0 | 0 | 
 | 5,2 | S5,S2 | 0 | 0 | 0 | 
AA | 6,1 | S6,S1 | Id | -Id | 0 | 
 | 1,2 | S1,S2 | Id | 0 | -Id | 
 | 4,5 | S4,S5 | -Id | 0 | Id | 
 | 5,6 | S5,S6 | 0 | -Id | Id | 
 | 3,4 | S3,S4 | -Id | Id | 0 | 
Active
states
Active vectors can be expressed as

## Slide 41
Active vectors form a regular hexagon with 6 equal sectors.
Zero vector lies on the center.

## Slide 42
Active vectors and zero vectors do not move in space and they are referred to stationary vectors.
Current reference vector rotates in space at an angular velocity ω = 2πf1
f1 is the required fundamental frequency of the inverter output current.
Angular displacement between and the α axis of the α-β plane is
For any position of it can be synthesized by three near by stationary vectors.
Magnitude of output current is adjusted by adjusting the length of reference phaor
and frequency by adjusting the speed of rotation

## Slide 43: Dwell Time Calculation
Let lies in sector I.
Inverter switches are controlled
such that, states of the inverter
shifts between states 1, 2 and 0 on a part time basis so that the resultant current vector agrees closely with
Sampling period Ts = T1 + T2 + T0
By the ampere- second balancing equation .
T1 , T2 and T0 are dwell times along

## Slide 44
Splitting this into real axis and imaginary axis components,

## Slide 45
Maximum value of reference vector Irefmax corresponds to the radius of the largest circle that can be inscribed in the hexagon.
Length of active vector is

## Slide 46
Trapezoidal PWM (TPWM)
vm is the trapezoidal modulating wave and vcr is a triangular carrier wave.
The amplitude modulation index is defined by
are the peak values of the modulating and carrier waves, respectively.
Only two devices conduct at a time, resulting in a defined iw.
The magnitude of iw is set by the dc current Id.

## Slide 47
Fundamental-frequency component Iw1 does not vary significantly with the modulation index ma.
When ma varies from zero to its maximum value of 1.0,
Iw1 changes from its minimum value of 0.89 Iw1max to Iw1max, presenting only an 11% increase.
This is due to the fact that iw is not modulated in the centre ∏/3 region of each half-cycle.
In practice, the adjustment of fundamental component Iw1 is accomplished by varying the dc current Id through the input side rectifier instead of varying ma.

## Slide 48
The switching frequency of the devices is fsw = f1 × Np
f1 is the fundamental frequency
Np is the number of pulses per half-cycle of iw.
Iwn is the rms value of the nth-order harmonic current in iw
Iw1max is the maximum of rms values of fundamental-frequency current
The PWM current iw does not contain any even-order harmonics since its waveform is of half-wave symmetry.
Np = 13 and ma = 0.85.
The TPWM scheme produces two pairs of dominant harmonics at
n = 3(Np – 1) ± 1 and
n = 3(Np – 1) ± 5,
which are the 31st, 35th, 37th, and 41st for Np=13.

## Slide 49: Selective Harmonic Elimination PWM
To eliminate a number of low-order unwanted harmonics in the inverter PWM current iw.
The switching angles are pre-calculated and then imported into a digital controller for implementation.

## Slide 50
The inverter PWM current iw can be expressed as
To eliminate k harmonics, k equations can be made by setting an = 0,