## Slide 1: Diode Clamped Multilevel Inverter
Three level Diode Clamped Inverter
DC bus voltage is split into 3 levels by two series connected capacitors
Output voltage Van has 3
levels
+Vd/2, 0, -Vd/2
>

## Slide 2
For Van = + Vd/2,
S1 and S2 are closed
For Van = - Vd/2,
and are closed
For Van = 0, and are closed
>
Vd/2
Vd/2

## Slide 3
When S1 and S2 are on ,
voltage across is
clamped to voltage across C1
through as Vdc/2
voltage across is clamped
to voltage across C2 through
as Vdc/2
>

## Slide 4
Five level Diode Clamped Inverter
Voltage across each
capacitor is Vd/4.
Voltage stress on each
device is limited to Vd/4.
>

## Slide 5
For Van = + Vdc/2,
S1 , S2 , S3 and S4 are closed
For Van = + Vdc/4,
S2 , S3 ,S4 and S’1 -are closed
For Van = 0,
S3 , S4, S’1 and S’2are closed
For Van = - Vdc/4,
S’1, S’2, S’3 and S4 are closed
For Van = - Vdc/2,
S’1, S’2, S’3 and S’4 are closed
>

## Slide 6
Each switching device is
required to block a voltage of
Vdc/(m-1) volts
Clamping diodes have different
reverse voltage rating
Let S1 , S2 , S3 and S4 are closed
Voltage across D1 is
Voltage across D2 is
Voltage across D3 is
Let S’1, S’2, S’3 and S’4 are closed
Voltage across D’1 is
Voltage across D’2 is
Voltage across D’3 is
For an m level inverter, number of diodes
required for one phase is (m-1)(m-2)
>

## Slide 7
DIODE CLAMPED MLI
Three Phase Three-Level DIODE CLAMPED MLI

## Slide 8
Each leg has four active switches S1 , S2 , S3 , S4 with
and four antiparallel diodes
D1 to D4.
The dc bus capacitor is split into
two each with a voltage of Vd/2
with respect to Z.
DZ1 and DZ2 are called
clamping diodes.
The capacitors are charged or discharged by neutral current iZ

## Slide 9
Switching states
Switching states of leg A
P denotes that the upper two
switches S1 and S2 of leg A
are on
Terminal voltage
vAZ = + E
N indicates that the
lower two switches conduct, and vAZ = – E.
Switching State (Phase A) | Device States (Phase A) |  |  |  | VAZ
 | S1 | S2 | S3 | S4 | 
P | ON | ON | OFF | OFF | E
O | OFF | ON | ON | OFF | 0
N | OFF | OFF | ON | ON | -E

## Slide 10
O signifies that the inner two switches
S2 and S3 are on and vAZ is clamped
to zero through the clamping diodes.
For a positive load current (iA > 0),
DZ1 is on, A is connected to Z through
DZ1 and S2. (iZ < 0)
For a negative load current (iA < 0),
DZ2 is on, A is connected to Z through S3 and DZ2. (iZ > 0)
Switching state | Device States (Phase A) |  |  |  | VAZ
 | S1 | S2 | S3 | S4 | 
P | ON | ON | OFF | OFF | E
O | OFF | ON | ON | OFF | 0
N | OFF | OFF | ON | ON | -E

## Slide 11
The waveform for vAZ has three voltage levels,
+E, 0, and –E
The gate signals can be generated by carrier-based modulation, space vector modulation, or selective harmonic elimination schemes etc.
PWM of 3 Level Diode Clamped MLI
OoOO
O
P
O
P
O
P
O
N
O
N
O
N
O

## Slide 12
The waveform for vAZ has three voltage levels,
+E, 0, and –E
The gate signals can be generated by carrier-based modulation, space vector modulation, or selective harmonic elimination schemes etc.
PWM of 3 Level Diode Clamped MLI
OoOO
O
P
O
P
O
P
O
N
O
N
O
N
O

## Slide 13: Terminal voltages and line to line voltage waveforms
vAZ, vBZ, and vCZ are three-phase balanced with a phase shift of 2π/3 between each other.
The line-to-line voltage vAB contains five voltage levels
(+2E, +E, 0, –E, and –2E).

## Slide 14
Commutation of switching devices
leg A
Assumptions
Load current iA is constant
during the commutation
interval due to the
inductive load
dc bus capacitors Cd1 and Cd2
are sufficiently large such that
the voltage across each
capacitor is kept at
constant value E
all the switches are ideal.

## Slide 15
Consider the transition from
switching state [O] (S2 & S3)
to [P] (S1 & S2)
S3 is turned off and S1 is
turned on.
A blanking time of δ is required
in between this.
S2
S3
S1
S2
S3
S4
S1
S2
S2
S3
S1
S2
S2
S3
S3
S4
S3
S4
S2
S3
S2
S3
S2
S3

## Slide 16
Commutation with iA > 0.
during switching state [O]
S1 and S4 are off ,
S2 and S3 are on.
Positive load current (iA > 0)
flows through the
clamping diode DZ1 and S2
vS2 = 0 = vS3
vS1 =
E
vS4 =
E

## Slide 17
during interval δ
S3 is being turned off ,
Path of iA remains unchanged
and flows through the
clamping diode DZ1 and S2
When S3 is completely switched off,
vS3 =
E/2
vS4 =
E/2

## Slide 18
during switching state [P]
S1 is gated on (vS1 = 0)
DZ1 is reverse-biased and turned off.
The load current iA is commutated
from DZ1 to S1
vS3 =
E
vS4 =
E.

## Slide 19
Commutation with iA < 0.
during switching state [O]
S1 and S4 are off ,
S2 and S3 are on.
Negative load current (iA < 0)
flows through the S3 and
clamping diode DZ2
vS2 = 0 = vS3
vS1 =
E
vS4 =
E

## Slide 20
during interval δ
S3 is being turned off ,
Negative inductive load current
iA flows through diodes
D1 and D2
vS1 ≈ 0 ≈ vS2
The load current is commutated
from S3 to the diodes.
During the commutation of S3, voltage across S4 is clamped to E due to DZ2
vS3 rises from zero to E and vS4 is kept at E.

## Slide 21
during switching state [P]
The turn-on of S1 does not affect the operation of the circuit.
S1 and S2 do not carry the load current due to the conduction of D1 and D2.

## Slide 22
all the switching devices withstand only half the supply voltage during commutation from [P] to [O] / [O] to [P] / [N] to [O] / [O] to [N] due to the clamping diodes.
Switching between [P] and [N] is not permitted.
Two switches are being turned
on and two switches are being turned off
Voltage sharing may not be same.
Switching loss is doubled.
Switching state | Device States (Phase A) |  |  |  | VAZ
 | S1 | S2 | S3 | S4 | 
P | ON | ON | OFF | OFF | E
O | OFF | ON | ON | OFF | 0
N | OFF | OFF | ON | ON | -E

## Slide 23
Each of the switches in the NPC inverter withstands only half of the total dc voltage during commutation.
Drawbacks of NPC inverter
additional clamping diodes,
possible deviation of neutral point voltage.

## Slide 24: SPACE VECTOR MODULATION IN THREE PHASE THREE LEVEL INVERTER
Stationary space vectors
Each inverter phase leg has
three switching states
[P], [O], and [N].
Total 33 = 27 possible combinations
of switching states represented
by 27 voltage vectors.
These voltage vectors can be
divided into four groups
  Zero vectors
  Small vectors
  Medium vectors
  Large vectors

## Slide 25
Space Vector | Switching State | Vector Classification | Vector magnitude
 | [PPP] [OOO][NNN] | Zero vector | 0
Zero vectors V0 ,
represent three zero switching states
[PPP], [OOO], and [NNN].
The magnitude of V0 is zero.

## Slide 26
 |  | P Type | N Type | Sma l L V E C T O r | Vd/3
Each small vector represents two switching states.
that containing [P] is called P-type small vector
that containing [N] is called N-type small vector
magnitude is Vd /3.
Small vectors (V1 to V6 ))
NNO
POO
ONN
PPO
OON
OPO
NON
OPP
NOO
OOP
POP
ONO

## Slide 27
Medium vectors
(V7 to V12 )),
magnitude is √ 3 Vd /3..
Large vectors
( V13 to V18),
magnitude of 2Vd/3.
PNP
Medium vector
Large Vector
PON
OPN
NPO
NOP
ONP
PNO
PNN
PPN
NPN
NPP
NNP

## Slide 28
SECTOR II
SECTOR I
SECTOR III
SECTOR IV
SECTOR V
SECTOR VI
Space vector diagram is divided into six triangular Sectors (I to VI)

## Slide 29
Each sector is further divided into four triangular regions (1 to 4) .
5
7
6
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
13
14
15
16

## Slide 30
desired output voltage of the three phase 3level inverter
Desired output peak magnitude is Vm*
desired output frequency is ω*.
This three phase system results in a reference space vector of magnitude Vm* that rotates with an angular velocity of
ω*.

## Slide 31
Inverter switches are controlled between the nearest 3 vectors of the region in which the tip of the reference phasor lies.
5
7
6
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
13
14
15
16

## Slide 32
Product of the reference voltage Vref and sampling period Ts
= V1 × interval allocated for state V1
+ V2 × interval allocated for state V2
+ V0 × interval allocated for state V0
When Vref lies in region1, inverter state is shifted between
based on volt-second balancing principle.
Dwell Time Calculation
v0, v1 and v2.

## Slide 33
Reference vector Vref can be synthesized by three nearest stationary vectors.
When Vref falls into region 2 of sector I , the three nearest vectors are
V1, V7 and V2
Let Ta, Tb, and Tc are the
dwell times for V1, V7, and
V2, respectively.
V1Ta + V7Tb + V2Tc = VrefTs
Ta + Tb + Tc = Ts

## Slide 34
The magnitudes of voltage vectors V1, V2, V7, and Vref are
V1Ta + V7Tb + V2Tc = VrefTs

## Slide 35
Equating real and imaginary parts

## Slide 36
Where
The maximum length of the reference vector Vrefmax corresponds to the radius of the largest circle that can be inscribed within the hexagon.
This is equal to the length of the medium voltage vectors.
Range of ma is

## Slide 37: Dwell time calculation for Vref in sector I

## Slide 38
Region 1
Region 2
Region 3
Region 4

## Slide 39: Relationship Between Vref Location and Dwell Times
When Vref moves towards V2 , longer will be the dwell time for V2
When Vref coincide with V2,
the dwell time Tc for V2 is Ts
Ta and Tb for V14 and V7 diminish to zero.
Assume that the head of Vref points to
the center Q of region 4,
Distances from Q to V2, V7, and V14
are the same.
The dwell times for these vectors
should be identical

## Slide 40
It depends on the switching state of the NPC inverter.
neutral point voltage vZ
voltage between the neutral point Z and the negative dc bus is defined as neutral point voltage vZ .
Voltage across Cd1 and Cd2 should be equal and exactly Vd/2.

## Slide 41
Switching sequence is selected after considering the following factors
Transition from one sector or
region to the next should
involve no or minimum
switching.
3. Neutral point voltage deviation should be minimum.
Design of Switching sequence
1. Transition from one switching state to the next should involve only two switches in the same leg.

## Slide 42
Assume that the inverter is in motoring mode.
Power flows from dc source to load.

## Slide 43
Effect of Switching States on Neutral-Point Voltage Deviation.
zero vector state V0 [PPP]
inverter terminals A, B, and C are
connected to the positive dc bus.
The neutral point Z is left
unconnected.
This switching state does not affect vZ.
other two zero switching states,
[OOO] and [NNN] also
do not cause vZ to shift.

## Slide 44
Effect of Positive small vector state on Vz
V1 [POO]
terminal A is connected to the
positive dc bus.
B and C are connected to Z.
neutral current iZ flows into Z, causing vZ to increase.

## Slide 45
Effect of Negative small vector state on Vz
V1 [ONN]
inverter terminals A is connected to Z.
B and C are connected to
negative dc bus.
neutral current iZ flows out of Z, causing vZ to decrease.

## Slide 46
Effect of Medium vector state
V7 [PON]
terminals A is connected to the
positive dc bus.
B is connected to Z.
C is connected to N.
Depending on the inverter operating conditions, the neutral-point voltage vZ may rise or drop.

## Slide 47
Effect of Large vector state
V13 [PNN]
terminals A is connected to the
positive dc bus.
B and C are connected to N.
Z is left unconnected. Hence, neutral-point voltage vZ is not affected.

## Slide 48
It can be summarized that
  Zero vectors V0 do not affect the neutral point voltage vZ.
  Small vectors V1 to V6 have influence on vZ.
  P-type small vectors make vZ increase,
  N-type small vectors cause vZ to decrease.
  Medium vectors V7 to V12 also affect vZ, but the direction of voltage deviation is undefined.
  The large vectors V13 to V18 do not affect neutral-point voltage.

## Slide 49
Switching sequence is selected after considering the following factors
Transition from one sector or
region to the next should
involve no or minimum
switching.
3. Neutral point voltage deviation should be minimum.
Design of Switching sequence
1. Transition from one switching state to the next should involve only two switches in the same leg.

## Slide 50
Switching Sequence with Minimal Neutral-Point Voltage Deviation.
A P-type small vector causes the neutral-point voltage vZ to rise while an N-type small vector makes vZ fall.
To minimize the neutral-point voltage deviation, dwell time calculated during one sampling period Ts for a small vector is equally divided to the two small vectors (P- and N-type switching states ) available at that point.

## Slide 51
  Case 1 One Vector among the three selected vectors is a small vector.
  Consider that Vref is in region 4 of Sector I.
  It can be synthesized by one small vector V2, one medium vector V7 and one large vector V14.
  The small vector V2 has two switching states [PPO] and [OON].
  To minimize the neutral voltage
  deviation, the dwell time for V2
  should be equally distributed
  between the states {[PPO] and [OON]}.

## Slide 52
  sampling period of the PWM pattern (Ts = Ta + Tb + Tc).
  During the transition from [OON] to [PON] S1 is turned on and S3 is turned off. Only two switches are involved.
  The dwell time Tc for small vector V2 is equally divided between the P- and N-type switching states.
  This minimizes the neutral point voltage deviation.
S2
S3
S1
S2
S1
S2
S1
S2
S2
S3
S1
S2
S1
S2

## Slide 53
  The transition for Vref moving from one sector (or region) to the next does not involve any switching,
Among the four switching devices in an inverter leg, only two are tuned on and off once per sampling period.
S1
S2
S2
S3
S1
S2
S1
S2
S1
S2
S2
S3
S1
S2

## Slide 54
Case 2: Two Small Vectors Among Three Selected Vectors.
To reduce the neutral voltage deviation, each of the two regions is further divided into two sub regions
Assume that Vref lies in region 2a.
It can be approximated by
V1, V2, and V7.
When Vref is in region 1 or 2 of sector I , two of the three selected vectors are small vectors.

## Slide 55
Since Vref is closer to V1 than V2, the corresponding dwell time Ta for V1 is longer than Tc for V2.
The vector V1 is referred to as
dominant small vector whose
dwell time is equally divided
between V1P and V1N .

## Slide 56
Vref is closer to V2 than V1, the corresponding dwell time Tc for V2 is longer than Ta for V1.
V2 is the dominant small vector
Its dwell time is equally divided
between V2P and V2N .
OON
PON
POO
PPO
POO
PON
OON
Tc/4
Tb/2
Ta/2
Tc/2
Ta/2
Tb/2
Tc/4

## Slide 57: Causes of Neutral-Point Voltage Deviation
In addition to the influence of small- and medium-voltage vectors, the neutral-point voltage may also be affected by
Unbalanced dc capacitors due to manufacturing tolerances
Inconsistency in switching device characteristics
Unbalanced three-phase operation
To minimize the neutral-point voltage shift, a feedback control scheme can be implemented, where the neutral-point voltage is detected and then controlled.

## Slide 58
Three level capacitor clamped (Flying Capacitor) MLI
For Van = + Vd/2,
S1 and S2 are closed
Van= Vc2 = Vd/2
For Van = - Vdc/2,
S’1 and S’2 are closed
Van= Vc2 = -Vdc/2
For Van = 0, S1 and S’1 are closed
or
S2 and S’2 are closed
+
-
+
-
+
-
a
n
n
a

## Slide 59
Five level capacitor clamped MLI
For Van = + Vdc/2,
S1 , S2 , S3 and S4 are closed
For Van = - Vdc/2,
S’1 , S’2 , S’3 and S’4 are closed
For Van = + Vdc/4,
1. S1 , S2 ,S3 and S’1 -are closed
Vd/2
-Vd/4
-Vd/2
-
+
+
+
-
-
Vd/4

## Slide 60
2. S4 , S3 , S2 and S’4 are closed
3. S4 , S3 , S’3 and S1 are closed
For Van = - Vdc/4,
1. S’1 , S’2 , S’3 and S1 are closed
2. S4 , S’2 , S’3 and S’4 are closed
3. S’1S3 S’3 and S’4are closed

## Slide 61
For Van = 0,
1. S1 , S2 , S’1 and S’2 are closed
2. S3 , S4 , S’3 and S’4 are closed
3. S1 , S3 , S’1 and S’3 are closed
4. S1 , S4 , S’2 and S’3 are closed
5. S2 , S4 , S’2 and S’4 are closed
6. S2 , S3 , S’1 and S’4 are closed